// Parameters for the simulation
grid_size = 200; // Grid size (NxN)
time_steps = 200; // Number of time steps
dx = 0.1; // Grid spacing
dt = 0.01; // Time step size
c = 1.0; // Speed of wave propagation

// Initialize the wave field (E-field)
wave_field = zeros(grid_size, grid_size);
wave_velocity = zeros(grid_size, grid_size);

// Define initial wave sources (photon-like oscillations)
sources = [
    floor(grid_size / 4), floor(grid_size / 4);
    floor(3 * grid_size / 4), floor(3 * grid_size / 4);
    floor(grid_size / 2), floor(grid_size / 2);
    floor(grid_size / 4), floor(3 * grid_size / 4);
    floor(3 * grid_size / 4), floor(grid_size / 4);
    floor(grid_size / 4), floor(grid_size / 2);
    floor(3 * grid_size / 4), floor(grid_size / 2);
    floor(grid_size / 2), floor(grid_size / 4);
    floor(grid_size / 2), floor(3 * grid_size / 4)
];

// Define source frequencies (randomized)
source_frequency = rand(1, size(sources, 1)) * 2 + 0.5; // Random between 0.5 and 2.5 Hz

// Display source information
disp("Wave Source Positions and Frequencies:");
for i = 1:size(sources, 1)
    printf("Source %d -> Position: (%d, %d), Frequency: %.2f Hz\n", i, sources(i, 1), sources(i, 2), source_frequency(i));
end

// Time-dependent source term
function wave_field = add_sources(wave_field, t, sources, source_frequency)
    for i = 1:size(sources, 1)
        x = int(sources(i, 1));
        y = int(sources(i, 2));
        freq = source_frequency(i);
        wave_field(x, y) = wave_field(x, y) + sin(2 * %pi * freq * t) * 50; // Amplify injection
    end
endfunction

// Update function for the wave equation
function [wave_field, wave_velocity] = update_wave(wave_field, wave_velocity, dt, dx, c)
    laplacian = (
        circshift(wave_field, [1, 0]) + circshift(wave_field, [-1, 0]) + ...
        circshift(wave_field, [0, 1]) + circshift(wave_field, [0, -1]) - ...
        4 * wave_field
    ) / dx^2;

    wave_velocity = wave_velocity + c^2 * laplacian * dt;
    wave_field = wave_field + wave_velocity * dt;
endfunction

// Initialize plot
x = 1:grid_size;
y = 1:grid_size;
scf();
h = gcf();
h.figure_name = "Photon Wave Field Simulation - Multiple Sources";
h.color_map = jetcolormap(128);
drawlater();
scaling_factor = 1e3; // Amplify for visibility

// Animation loop
for t = 1:time_steps
    // Add sources
    wave_field = add_sources(wave_field, t * dt, sources, source_frequency);

    // Update wave propagation
    [wave_field, wave_velocity] = update_wave(wave_field, wave_velocity, dt, dx, c);

    // Apply light damping at boundaries
    wave_field(1, :) = wave_field(2, :) * 0.95;
    wave_field(grid_size, :) = wave_field(grid_size-1, :) * 0.95;
    wave_field(:, 1) = wave_field(:, 2) * 0.95;
    wave_field(:, grid_size) = wave_field(:, grid_size-1) * 0.95;

    // Amplify and Normalize
    wave_field_display = wave_field * scaling_factor;
    max_amplitude = max(wave_field_display(:));
    min_amplitude = min(wave_field_display(:));

    if max_amplitude == min_amplitude
        max_amplitude = 1;
    end

    wave_field_display = (wave_field_display - min_amplitude) / (max_amplitude - min_amplitude);

    // Update plot
    clf();
    Matplot(wave_field_display);
    xtitle("Photon Wave Field Simulation - Multiple Sources");
    colorbar();
    sleep(50); // Pause for visualization
    drawnow();
end

disp("Simulation complete!");